## Slide 1: Lab. 04
Logic Design Lab.
Spring 2018
Prof. Chang-Gun Lee
(cglee@snu.ac.kr)
TA. WonJae Jang
TA. Wonseok Lee
TA. Alena Kazakova
TA. Dongwan Kang
(ta@rubis.snu.ac.kr)

## Slide 2: Contents
Multiplexer, Demultiplexer
Encoder, Decoder
Verilog
Lab
  Implement a Decoder using Verilog
  Implement a 3-to-8 Decoder using a 2-to-4 Decoder
Homework (due 10th, April)

## Slide 3: Multiplexer, Demultiplexer

## Slide 4: Multiplexer and Demultiplexer
2n inputs, 1 outputs
Selection lines exist
1 inputs, 2n outputs
Selection lines exist
Notes: 모르는지 물어보고 요청하면 그려줄 것.

## Slide 5: Encoder, Decoder

## Slide 6: Encoder, Decoder
n inputs, 2n outputs
Selects one of 2n outputs by decoding the binary value on the n inputs
No selection lines exist
2n inputs, n outputs
Outputs the binary value of the selected input
No selection lines exist

## Slide 7: Verilog

## Slide 8: Overview
Hardware description languages (HDLs)
  We will focus on Verilog
Verilog Basics
  Verilog Notations
  Verilog Operators
  Verilog Keywords & Constructs
Types of programming (description)
  Structural description
  Data-flow style description
  Behavioral description

## Slide 9: Hardware description languages (HDLs)
2018 Spring LDLAB HW
Hard to understand
Too many papers…
   Let’s make standard HDL !
SystemVerilog
Verilog
VHDL
Superset extension
FOCUS

## Slide 10: Verilog Basics : Verilog Notations (1)
Verilog is:
  Case sensitive
  Based on the programming language C
Comments:
  // this is a comment Single line
  /* this is a comment */ Multiple line
Statement terminator:
  Every statement should be terminated with ; (semi-colon)

## Slide 11: Verilog Basics : Verilog Notations (2)
Literals
  [bit_size]’[base_format][value]
  Example > below literals represent same value
  8’b10100001
  8’hA1
  8’d161
Identifiers
  Scalar (always 1 bit)
    Example > below identifiers are similar with single variable in C
    A, B, myA, myB…
  Vector (bit size is specified as [high_bit:low_bit])
    Example > below identifiers are similar with array variable in C
    arrA[7:0], arrB[15:0], arrMyA[7:0], arrMyB[15:0]…

## Slide 12: Verilog Basics : Verilog Operators (1)
Bitwise Operators
  ~ NOT
  & AND
  | OR
  ^ XOR
  Example >
ex1
ex_in0[0]
ex_in1[0]
ex_in0[1]
ex_in1[1]
ex_in0[2]
ex_in1[2]
ex_in0[3]
ex_in1[3]
ex_out[0]
ex_out[1]
ex_out[2]
ex_out[3]
Notes: Paradigm shift 설명. RHS 변화할 때 마다 바뀜.
Wire의 Textural form일 뿐.

## Slide 13: Verilog Basics : Verilog Operators (2)
Logical & Relational Operators
  &&, | |, = =, !=, >=, <=, >, <, etc.
Arithmetic Operators
  +, -, etc.
Concatenation Operators
  {identifier_1, identifier_2, …}
  Examples >
  {ex_in0[1:0],ex_in1[3:2]}

## Slide 14: Verilog Basics : Verilog Keywords & Constructs (1)
Module declaration
  Start with module, end with endmodule
Module IO port declaration
  Inputs use keyword, input, Outputs use keyword output.
Example >
ex1
Notes: Paradigm Shift RECAP 순서와 상관 없음.
위자드가 있음.

## Slide 15: Verilog Basics : Verilog Keywords & Constructs (2)
Wire Declaration
  Scalar Example : wire t1, t2;
  Vector Example : wire[7:0] t1, t2;
Example >
tmp
Error
Notes: 중간에 Temporal wire를 사용하는 경우.
항상 이미지를 가지고 코딩.

## Slide 16: Verilog Basics : Verilog Keywords & Constructs (3)
Primitive Gates
  buf, not, and, or, nand, nor, xor, xnor
  Syntax:
  [gate_operator] [instance_identifier] [(output, input_1, input_2, …)]
  Example >

## Slide 17: Verilog Basics : Verilog Keywords & Constructs (4)
Process
  The body of a process consists of procedural statement to make desired outputs from inputs as like a common programming
    initial – executes only once beginning at t = 0.
      Syntax: initial Statement;
      Example > initial begin Statement; Statement; … end
    always – executes at t = 0 and repeatedly thereafter following repeat conditions.
      Syntax: always Repeat condition Statement;
      Example > always Repeat condition begin Statement; Statement; … end
Notes: 빠르게 설명, 예제로 보여줄 것임.

## Slide 18: Verilog Basics : Verilog Keywords & Constructs (5)
  Timing Control Statement (for repeat conditions)
  The body of the process consists of procedural assignments
    Blocking assignments
      Example: C = A + B;
      Execute sequentially as in a programming language
    Non-blocking assignments
      Example: C <= A + B;
      Evaluate right-hand sides, but do not make any assignment until all right-hand sides evaluated. Execute concurrently unless delays are specified.
Type | Syntax | Description
Delay Control | #10 | Delay 10 unit time
Event Control | @(a) | Wait until signal ‘a’ is changed
 | @(posedge a) @(negedge a) | Wait until signal ‘a’ is changed to ‘1’ Wait until signal ‘a’ is changed to ‘0’
Level Control | wait (a==0) | Wait until signal ‘a’ is equal to ‘0’
Notes: 빠르게 설명, 예제로 보여줄 것임.

## Slide 19: Verilog Basics : Verilog Keywords & Constructs (6)
Examples > blocking vs. Non-blocking
  Always @(*)
  begin
  B = A;
  C = B;
  end
  Suppose initially A = 0, B = 1, and C = 2. After execution, B = 0 and C = 0.
  Always @(*)
  begin
  B <= A;
  C <= B;
  end
  Suppose initially A = 0, B = 1, and C = 2. After execution, B = 0 and C = 1.
Notes: 빠르게 설명, 예제로 보여줄 것임.

## Slide 20: Verilog Basics : Verilog Keywords & Constructs (7)
Because of the use of procedural rather than continuous assignment statements, assigned values must be retained over time.
  Register type: reg
  The reg in contrast to wire stores values between executions of the process
  A reg type does not imply hardware storage!
Notes: 빠르게 설명, 예제로 보여줄 것임.

## Slide 21: Verilog Basics : Verilog Keywords & Constructs (8)
Conditional constructs
  The if-else
    If (condition)
    begin procedural statements end
    {else if (condition)
    begin procedural statements end}
    else
    begin procedural statements end
  The case
    case expression
    {case expression : statements}
    endcase;
Notes: 빠르게 설명, 예제로 보여줄 것임.

## Slide 22: Types of programming (description)
Describe hardware at varying levels of abstraction
  Structural description
    Textual replacement for schematic
  Data-flow style description
    Textual replacement of truth table
  Behavioral/functional description
    Define just WHEN, WHAT, not HOW

## Slide 23: Tutorials

## Slide 24: 1. Design Structure
=
+
Notes: 모든 방법론의 공통 사항.
버블 설명.
아까 말한 위자드.
하프를 3가지 방법으로 해볼 것임.

## Slide 25: 2-1. Structural Description
N_B
N_A
N_G
Textual representation of schematic
Notes: 그냥 스키마틱을 텍스트로 표현한 형태의 디자인.

## Slide 26: 2-2. Data Flow Description
B | A | G | Y[3:0]
0 | 0 | 0 | 1110
0 | 1 | 0 | 1101
1 | 0 | 0 | 1011
1 | 1 | 0 | 0111
0 | 0 | 1 | 1111
0 | 1 | 1 | 1111
1 | 0 | 1 | 1111
1 | 1 | 1 | 1111
Textual representation of truth table
Notes: 그냥 진리표를 옮긴 형태의 디자인.
삼항 연산자, sensitive list in wire.

## Slide 27: 2-3. Behavioral Description
When?
Which action?
If there is no else-block,
reg out will be synthesized as storage

## Slide 28: 2-4. Unify Modules
It is same as using gate primitives

## Slide 29: Lab

## Slide 30: Today
1. Design a 74x139 using Verilog.
  Practice all the designing methods for half 74x139 each and simulate them
  Implement a 74x139 and simulate it
2. Design a 3-to-8 decoder using 2-to-4 decoders only and simulate it.

## Slide 31: Create a new Verilog project

## Slide 32: Set the project name, location, type

## Slide 33: Set the project name, location, type

## Slide 34: Create a new Verilog source

## Slide 35: Create a new Verilog source
or

## Slide 36: Write your own Verilog codes

## Slide 37: Compile and check errors

## Slide 38: Create a Verilog test bench

## Slide 39: Write a Verilog test bench codes

## Slide 40: Simulate it

## Slide 41: Simulation result

## Slide 42: Homework

## Slide 43: Homework
Implement 4-to-1 MUX with all the designing methods that we practiced and Simulate it.
(2) Discuss about each type of descriptions.
  (Pros & Cons, etc.)

## Slide 44: Report
Write a report
  # of pages doesn’t matter
  Documents should be submitted as PDF file.
  The file size should be less than 15Mb.
  Due : April, 10th (Before class begin at 7:00pm)

## Slide 45: NOTICE !!!
SUBMISSION FORMAT
  MAIL TITLE : LDLAB_170328_조_이름_학번
    Ex > LDLAB_170328_01_홍길동_2017-12345
  ATTACHED FILE NAME : LDLAB_170328_조_이름_학번.pdf
    Ex > LDLAB_170328_01_홍길동_2017-12345.pdf
Attach
  your simulation screen captures,
  source codes of your implementation,
  source codes of your simulation,
  at a single pdf file !!!