## Slide 1: Lab. 06
Logic Design Lab.
Spring 2018
Prof. Chang-Gun Lee
(cglee@snu.ac.kr)
TA. WonJae Jang
TA. Wonseok Lee
TA. Alena Kazakova
TA. Dongwan Kang
(ta@rubis.snu.ac.kr)

## Slide 2: Contents
FPGA
SNU Logic Design Board
Sample Implementation
Lab

## Slide 3: FPGA

## Slide 4: What is FPGA?
without FPGA
with FPGA
FPGA

## Slide 5: SNU Logic Design Board

## Slide 6: SNU Logic Design Board

## Slide 7: SNU Logic Design Board
I/O Connectors

## Slide 8: SNU Logic Design Board
Connect to PC with Xilinx Platform Cable USB
  HALT/RST Pin(Gray pin) not used.
  Make sure both board and USB are powered on.

## Slide 9: Sample Implementation

## Slide 10: Sample Implementation
Create new project, build a half adder schematic.
For detailed settings, refer to guidelines in Lab03.

## Slide 11: Sample Implementation
Design tab > User Constraints > I/O Pin Planning(PlanAhead) – Post-Synthesis.
Click ‘Yes’ to start PlanAhead, and to create an UCF file.

## Slide 12: Sample Implementation
Assign I/O pins for the half adder
RUBIS

## Slide 13: Sample Implementation
Design tab > double click Configure Target Device
Click OK to create an iMPACT file.
RUBIS

## Slide 14: Sample Implementation
Double click “Boundary Scan”.
RUBIS

## Slide 15: Sample Implementation
Right click on the right window > click ‘Initialize Chain’.
RUBIS

## Slide 16: Sample Implementation
Choose the schematic source you’ve written.
RUBIS

## Slide 17: Sample Implementation
Check settings > ‘OK’.
RUBIS

## Slide 18: Sample Implementation
Program FPGA Only > Program Succeeded
RUBIS

## Slide 19: Sample Implementation
Debug using assigned I/O ports. (This case, LEDs and tactile SWs.)
RUBIS

## Slide 20: LAB

## Slide 21: Today
(1) Implement ripple-carry adder, shown below, in Verilog, (2) and program it on the FPGA board.
Hint: 5 inputs (tactile SWs), 3 outputs (LEDs)
(a) Half Adder
(b) Full Adder
(c) Ripple Carry Adder

## Slide 22: Homework
RUBIS
22
1-bit Arithmetic Logic Unit (ALU).
  (1) Follow specification(a). Implement in Verilog. (M, S1, S0) are control inputs, (Ai, Bi) are data inputs, and (Fi) is outputs.
  (2) Simulate all possible outputs using Verilog test bench.
(a) specification
M | S1 | S0 | Function | Comment
0 | 0 | 0 |  | load
0 | 0 | 1 |  | complement
0 | 1 | 0 |  | xor
0 | 1 | 1 |  | xnor
1 | 0 | 0 |  | load
1 | 0 | 1 |  | complement
1 | 1 | 0 |  | Add (ignore carry)
1 | 1 | 1 |  | Complement and add (ignore carry)
M | S1 | S0 | Function | Comment
0 | 0 | 0 |  | load
0 | 0 | 1 |  | complement
0 | 1 | 0 |  | xor
0 | 1 | 1 |  | xnor
1 | 0 | 0 |  | load
1 | 0 | 1 |  | complement
1 | 1 | 0 |  | Add (ignore carry)
1 | 1 | 1 |  | Complement and add (ignore carry)