## Slide 1: Lab. 03
Logic Design Lab.
Spring 2018
Prof. ChangGun Lee
(cglee@snu.ac.kr)
TA. Wonjae Jang
TA. Wonseok Lee
TA. Dongwan Kang
TA. Alena Kazakova
(ta@rubis.snu.ac.kr)

## Slide 2: Contents
Two-bit comparator
Xilinx ISE
Universal Board
Lab

## Slide 3: Course Information
Assignment (report)
  Submission: ta@rubis.snu.ac.kr
  Weekly task
  Korean/English
  Single file, no page limit, .pdf
  Your report should include:
    Lab result (proof/alibi)
    Through discussion
    Homework (if there is any)
  Total size should be less than 15Mb (Do not use external download)
  Due: Before start of next class (7:00pm)
    - Late Policy: +24h: -20%, +48h: -50%, +72h: -100%
  File name and e-mail title should be written correctly (See the details next slide)

## Slide 4: Double check your e-mail/file format
LDLAB_YYMMDD_team#_NAME_StudentID
YYMMDD: Lab class date. Not the submission date.
  Ex) e-mail: LDLAB_170321_31_홍길동_2017-77777
    File : LDLAB_170307_31_홍길동_2017-77777.pdf
    LDLAB_170307_31_GildongHong_2017-77777.pdf

## Slide 5: Two Bit Comparator

## Slide 6: Block Diagram & Truth Table

## Slide 7: Karnaugh Map for EQ
K-map for EQ
1 0
0 1
0 0
0 0
D
A
0 0
0 0
1 0
0 1
B
C
A' B' C' D' + A' B C' D + A B C D + A B' C D’
= (A xnor C) • (B xnor D)

## Slide 8: Design Example
A B C D
EQ
EQ
XNOR is implemented with at least 3 simple gates
ver. 1
ver. 2
A' B' C' D' + A' B C' D + A B C D + A B' C D’
(A xnor C) • (B xnor D)
Two alternative implementations of EQ

## Slide 9: Xilinx ISE

## Slide 10: Xilinx ISE Design Suite
Integrated Synthesis Environment(ISE)
Release 14.7, 2013
Features
  Synthesis(compile) and analysis of HDL1) designs.
  Timing analysis, RTL diagram
  Xilinx FPGA programmer
1) HDL: Hardware Description Language

## Slide 11: Creating New Project
Select File -> New Project
Specify Name, Location, Working Directory. Select Top-level source type as Schematic.

## Slide 12: Project Settings
Set Project Settings as above
Click Next  Finish

## Slide 13: Creating Schematic
Right-Click anywhere in Hierarchy in Design tab, select New Source.
New Source Wizard window appears. Select Source Type window, select Schematic and type the File name. Ensure Add to project is checked.

## Slide 14: 2-input-AND gate circuit (1)
In Symbols tab, type “and” under Symbol Name Filter.
Select and2 under Symbols, and place it on board.
Click I/O Marker button and you can add input/output markers to your circuit.

## Slide 15: 2-input-AND gate circuit (2)
Change the names of input/output symbols.
Save to apply changes

## Slide 16: Creating Verilog Test Bench
Select New Source by right clicking inside Design tab.
Select Verilog Test Bench. Type the file name as above.

## Slide 17: Schematic Simulation Code

## Slide 18: Simulate Behavioral Model
Save the project
Ensure that Design tab is selected, View is set to Simulation, and your simulation source code is clicked
Double click Behavioral Check Syntax for syntax check
Double click Simulate Behavioral Model

## Slide 19: Simulation Result
To adjust the view, select View -> Zoom -> To Full View.

## Slide 20: Tips: Connecting multiple gates
When connecting multiple gates using ‘Add Wire’ button, make sure that both two ends don’t have I/O markers
No!
No!
Yes!

## Slide 21: Universal Board

## Slide 22: Custom-Made Universal Board
2-Pin Power Connector
LED
PCB Support Plastic
+
-
VCC
GND
SIG
(Electrically
connected
line)

## Slide 23: Turning it on using power supply
VCC
GND
3
1
2
Set voltage to 5V
using this button
4
Connect the
universal board
using power connecter

## Slide 24: Tips: Look up the datasheet!
NEVER trust the sorted device boxes… Always check the product name to confirm that you picked the right one.
Always look up the datasheet online, double check its pin mapping.
7486 XOR gate

## Slide 25: Lab

## Slide 26: Today
Implement 2-bit comparator LT, EQ, GT using Xilinx ISE Schematic. Simulate its behavior using Xilinx test bench.

## Slide 27: Homework
[TEAM]
Implement 2-bit comparator GT logic on the universal board, using DIP switch and primitive logic gates(INV, AND, OR, XOR, NAND…). Try your best to minimize the number of logic gates/chips used.

## Slide 28: Report
Write a report
  # of pages doesn’t matter
  Documents should be submitted as PDF file.
  All the files should be compressed to ZIP format.
  The file size should be less than 15Mb.
  Due : April, 3rd (Before class begins at 7:00pm)