## Slide 1: Lab. 07
Logic Design Lab.
Spring 2018
Prof. Chang-Gun Lee
(cglee@snu.ac.kr)
TA. WonJae Jang
TA. Wonseok Lee
TA. Alena Kazakova
TA. Dongwan Kang
(ta@rubis.snu.ac.kr)

## Slide 2: Sequential logic

## Slide 3: Sequential logic (1)
Output is determined by both of current state and input
To save current state, feedback is used to implement storage
Example > sequential logic
  If input == 0 then hold current status, else if input == 1 then toggle current status.
  Output is same as current status.
current_status | input | output
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
current_status
input
output

## Slide 4: Sequential logic (2)
current_status
input
output
Taxonomy …
Never mind, always work (race O)
   Latch
Work only when it is enabled (race O)
   Gated latch
Work only when it is edge triggered (race X)
   Flip-flop

## Slide 5: R-S Latch

## Slide 6: R-S Latch
S R Q(t) Q(t+) 0 0 0 0 0 0 1 1 0 1 0 0 0 1 1 0 1 0 0 1 1 0 1 1 1 1 0 X 1 1 1 X
hold
reset
set
not allowed
R-S latch is a 1 bit memory with cross-coupled gates.
RS Q | 00 | 01 | 11 | 10
0 |  | 1 | X | 
1 | 1 | 1 | X | 
Notes: 가장 기본이 되는 컴포넌트. Q라는 state를 저장하는 역할을 한다. T+delta

## Slide 7: Gated R-S Latch
R and S(inputs) matter only when E(enable) = 1
Otherwise, hold current state
Notes: Enable이 clock으로 대체하는것 자세히 설명. Nor게이트 and로 바꾸기

## Slide 8: Clock

## Slide 9: Clock
Provide timing to sequential logic (ex. Flip-Flop)
Notes: State machine 설명. Timing이 state에 영향을 미침. 친숙한 ch3 oscillator 사용해서 설명. Wire사이 영향 미침
Timing을 동기화 시켜주는게 중요. Clock 개념

## Slide 10: Simple Oscillator
ENABLE
FEEDBACK
#0
#5
How to implement gate delay ?
Example >
wire tmp;
assign #5 tmp = tmp & 1;
Notes: State machine 설명. Timing이 state에 영향을 미침. 친숙한 ch3 oscillator 사용해서 설명. Wire사이 영향 미침
Timing을 동기화 시켜주는게 중요. Clock 개념

## Slide 11: Lab

## Slide 12: Today
Implement the following in Verilog and simulate the behavior.
(1) a R-S latch
(2) a gated R-S latch using (1)
(3) an simple oscillator

## Slide 13: Report
Write a report
  # of pages doesn’t matter
  Documents should be submitted as PDF file.
  The file size should be less than 15Mb.
  Due : May, 8th (Before class begins at 7:00pm)

## Slide 14: Homework
No Homework !