## Slide 1: Lab. 08
Logic Design Lab.
Spring 2018
Prof. Chang-Gun Lee
(cglee@snu.ac.kr)
TA. WonJae Jang
TA. Wonseok Lee
TA. Alena Kazakova
TA. Dongwan Kang
(ta@rubis.snu.ac.kr)

## Slide 2: Notice
Your midterm exam score has been uploaded at below link.
  https://rubis.snu.ac.kr/logic_design_2018_spring/3324177
  Claim schedule:
  2018.05.10 (THU) 12:00 - 13:30 at B301-R415
  2018.05.11 (FRI) 15:00 - 17:00 at B301-R415
  If you have another schedule on both of above schedules, please contact us ( ta@rubis.snu.ac.kr )

## Slide 3: Flip-Flops (1)
RECAP (last week lab…)
Never mind, always work (race O)
   Latch
Work only when it is enabled (race O)
   Gated latch
Work only when it is edge triggered (race X)
   Flip-flop
current_status
input
output

## Slide 4: Flip-Flops (2)

## Slide 5: Registers (1)

## Slide 6: Registers (2)
CLRb | MODE |  | CLK | SERIAL |  | PARALLEL |  |  |  | PARALLEL |  |  |  |  | 
 | S1 | S0 |  | SDL | SDR | D3 | D2 | D1 | D0 | Q3(t+1) | Q2(t+1) | Q1(t+1) | Q0(t+1) |  | 
0 | X | X | X | X | X | X | X | X | X | 0 | 0 | 0 | 0 |  | // CLEAR
1 | X | X | - | X | X | X | X | X | X | Q3(t) | Q2(t) | Q1(t) | Q0(t) |  | // NO CHANGE
1 | 1 | 1 | ↑ | X | X | d3 | d2 | d1 | d0 | d3 | d2 | d1 | d0 |  | // PARALLEL LOAD
1 | 1 | 0 | ↑ | 0 | X | X | X | X | X | Q2(t) | Q1(t) | Q0(t) | 0 |  | // SHIFT LEFT
1 | 1 | 0 | ↑ | 1 | X | X | X | X | X | Q2(t) | Q1(t) | Q0(t) | 1 |  | 
1 | 0 | 1 | ↑ | X | 0 | X | X | X | X | 0 | Q3(t) | Q2(t) | Q1(t) |  | // SHIFT RIGHT
1 | 0 | 1 | ↑ | X | 1 | X | X | X | X | 1 | Q3(t) | Q2(t) | Q1(t) |  | 
1 | 0 | 0 | ↑ | X | X | X | X | X | X | Q3(t) | Q2(t) | Q1(t) | Q0(t) |  | // HOLD

## Slide 7: Registers (3)
Nobody want to implement above complex circuit !!!
Behavioral Model of Verilog will save us

## Slide 8: Example (1)
Let’s implement the above sequential logic (4-bit register) using Verilog
  Step1. Implementing 4-bit register with asynchronous reset
  Step2. Verifying logic through simulation
CLRb | MODE |  | CLK | SERIAL |  | PARALLEL |  |  |  | PARALLEL |  |  |  |  | 
 | S1 | S0 |  | SDL | SDR | D3 | D2 | D1 | D0 | Q3(t+1) | Q2(t+1) | Q1(t+1) | Q0(t+1) |  | 
0 | X | X | X | X | X | X | X | X | X | 0 | 0 | 0 | 0 |  | // CLEAR
1 | X | X | - | X | X | X | X | X | X | Q3(t) | Q2(t) | Q1(t) | Q0(t) |  | // NO CHANGE
1 | 1 | 1 | ↑ | X | X | d3 | d2 | d1 | d0 | d3 | d2 | d1 | d0 |  | // PARALLEL LOAD
1 | 1 | 0 | ↑ | 0 | X | X | X | X | X | Q2(t) | Q1(t) | Q0(t) | 0 |  | // SHIFT LEFT
1 | 1 | 0 | ↑ | 1 | X | X | X | X | X | Q2(t) | Q1(t) | Q0(t) | 1 |  | 
1 | 0 | 1 | ↑ | X | 0 | X | X | X | X | 0 | Q3(t) | Q2(t) | Q1(t) |  | // SHIFT RIGHT
1 | 0 | 1 | ↑ | X | 1 | X | X | X | X | 1 | Q3(t) | Q2(t) | Q1(t) |  | 
1 | 0 | 0 | ↑ | X | X | X | X | X | X | Q3(t) | Q2(t) | Q1(t) | Q0(t) |  | // HOLD

## Slide 9: Example (2)
Step1. Implementing 4-bit register with asynchronous reset

## Slide 10: Example (3)
Step2. Verifying logic through simulation

## Slide 11: Today’s Lab
With Verilog:
Implement 4-bit Universal Shift Register
Verify 4-bit Universal Shift Register through simulation
CLRb | MODE |  | CLK | SERIAL |  | PARALLEL |  |  |  | PARALLEL |  |  |  |  | 
 | S1 | S0 |  | SDL | SDR | D3 | D2 | D1 | D0 | Q3(t+1) | Q2(t+1) | Q1(t+1) | Q0(t+1) |  | 
0 | X | X | X | X | X | X | X | X | X | 0 | 0 | 0 | 0 |  | // CLEAR
1 | X | X | - | X | X | X | X | X | X | Q3(t) | Q2(t) | Q1(t) | Q0(t) |  | // NO CHANGE
1 | 1 | 1 | ↑ | X | X | d3 | d2 | d1 | d0 | d3 | d2 | d1 | d0 |  | // PARALLEL LOAD
1 | 1 | 0 | ↑ | 0 | X | X | X | X | X | Q2(t) | Q1(t) | Q0(t) | 0 |  | // SHIFT LEFT
1 | 1 | 0 | ↑ | 1 | X | X | X | X | X | Q2(t) | Q1(t) | Q0(t) | 1 |  | 
1 | 0 | 1 | ↑ | X | 0 | X | X | X | X | 0 | Q3(t) | Q2(t) | Q1(t) |  | // SHIFT RIGHT
1 | 0 | 1 | ↑ | X | 1 | X | X | X | X | 1 | Q3(t) | Q2(t) | Q1(t) |  | 
1 | 0 | 0 | ↑ | X | X | X | X | X | X | Q3(t) | Q2(t) | Q1(t) | Q0(t) |  | // HOLD

## Slide 12: Homework
With Verilog:
  Implement & Simulate 8-bit Universal Shift Register
Write a report:
  # of pages doesn’t matter
  Documents should be submitted as PDF file.
  The file size should be less than 15Mb.
  Due : May, 15th (Before class begins at 7:00pm)
CLRb | MODE |  | CLK | SERIAL |  | PARALLEL |  |  |  |  |  |  |  | PARALLEL |  |  |  |  |  |  |  |  | 
 | S1 | S0 |  | SDL | SDR | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | Q7(t+1) | Q6(t+1) | Q5(t+1) | Q4(t+1) | Q3(t+1) | Q2(t+1) | Q1(t+1) | Q0(t+1) |  | 
0 | X | X | X | X | X | X | X | X | X | X | X | X | X | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  | // CLEAR
1 | X | X | - | X | X | X | X | X | X | X | X | X | X | Q7(t) | Q6(t) | Q5(t) | Q4(t) | Q3(t) | Q2(t) | Q1(t) | Q0(t) |  | // NO CHANGE
1 | 1 | 1 | ↑ | X | X | d7 | d6 | d5 | d4 | d3 | d2 | d1 | d0 | d7 | d6 | d5 | d4 | d3 | d2 | d1 | d0 |  | // PARALLEL LOAD
1 | 1 | 0 | ↑ | 0 | X | X | X | X | X | X | X | X | X | Q6(t) | Q5(t) | Q4(t) | Q3(t) | Q2(t) | Q1(t) | Q0(t) | 0 |  | // SHIFT LEFT
1 | 1 | 0 | ↑ | 1 | X | X | X | X | X | X | X | X | X | Q6(t) | Q5(t) | Q4(t) | Q3(t) | Q2(t) | Q1(t) | Q0(t) | 1 |  | 
1 | 0 | 1 | ↑ | X | 0 | X | X | X | X | X | X | X | X | 0 | Q7(t) | Q6(t) | Q5(t) | Q4(t) | Q3(t) | Q2(t) | Q1(t) |  | // SHIFT RIGHT
1 | 0 | 1 | ↑ | X | 1 | X | X | X | X | X | X | X | X | 1 | Q7(t) | Q6(t) | Q5(t) | Q4(t) | Q3(t) | Q2(t) | Q1(t) |  | 
1 | 0 | 0 | ↑ | X | X | X | X | X | X | X | X | X | X | Q7(t) | Q6(t) | Q5(t) | Q4(t) | Q3(t) | Q2(t) | Q1(t) | Q0(t) |  | // HOLD